## Slide 1
Dave Biersach
Brookhaven National Laboratory
dbiersach@bnl.gov
Foundations of
Quantum Information Science (QIS 101)
Session 21
Digital Circuits

## Slide 2: Session 21 – Goals
Understand Classical (Boolean) Digital Logic Circuits
  Review base conversion (binary2  decimal10)
  Analyze the three classical logic gates: NOT, AND, and OR
  Learn how to chain multiple logic gates together in a circuit
  Develop truth tables and calculate input & output states
  Understand how half-adders and full-adders operate
  Appreciate how memory and counters are constructed from gates
Simulate digital circuits using matrix algebra
  Represent gates via their action operators
  Combine multiple inputs using the tensor product of matrices

## Slide 3: Base Conversion – Binary to Decimal
10110012 = 8910
Most Significant Bit (MSB)
Least Significant Bit (LSB)
 LSB
 MSB
Position 0
Position 6

## Slide 4: Base Conversion – Decimal to Binary
11310 = 11100012
Most Significant Bit (MSB)
Least Significant Bit (LSB)
 LSB
 MSB
% = Remainder (Mod)
// = Floor (Integer)

## Slide 5: Run Cell 1 – base_conversion.ipynb








## Slide 6: Run Cell 2 – base_conversion.ipynb







## Slide 7: Run Cell 3 – base_conversion.ipynb




Knowing how to represent the decimal numbers 0 to 255 in binary (base 2) is very useful in quantum computing

## Slide 8: George Boole (1815 – 1864)
English mathematician
1847 published rules of symbolic logic (“Boolean Algebra”)
Only person with a data type named after him (“bool”)

## Slide 9: Boolean Logic Gates
Logic Gates
  Three types: NOT (inverter), AND, OR
  Gates have 1 or 2 input lines, and 1 output line
Input / Output lines are either:
  False, F, Cold, Low, L, 0 (Zero)
  True, T, Hot, High, H, 1
The left side of a truth table is counted using Base 2 to ensure every possible permutation of input states is evaluated across the entire circuit

## Slide 10: Boolean Logic Gates

## Slide 11: Boolean Logic Gates
NOT (inversion) is sometimes shown as a “bar” on top
OR is a “sum” while AND is a “multiply” (modulo 2)
  OR is sometimes shown as A + B
  AND is sometimes shown as A • B
Circuits flow (propagate state) from “Left to Right”
  The output of one gate flows into the input(s) of the next gate(s)
  We can evaluate a gate’s output line only when we know the value for every input line entering that gate

## Slide 12: NAND and NOR Gates

## Slide 13: Chaining Logic Gates
AND
NOT
OR
AND
NOT

## Slide 14: Multi-Input Gates

## Slide 15: Wire Overlap vs. Intersection
Use filled circles only for electrical junction points
Carry forward current logic state of line into each branch

## Slide 16: XOR Gate

## Slide 17: Truth Tables
1
1
1
1
0
1
0
0
1
0
1

## Slide 18: Truth Tables
With 3 input lines, there should be rows in the circuit’s truth table (0-7)

## Slide 19: Simple Circuit
Complete this Truth Table
1
1
0
1
1
1
1
1
1
0

## Slide 20: Logic Gates in the Real World

## Slide 21: Gate Equivalence
Augustus De Morgan’s laws:
  Can make an AND gate from 3 NOTs and 1 OR
  Can make an OR gate from 3 NOTs and 1 AND
  Simply invert both inputs and the output!
OR from AND
AND from OR

## Slide 22: De Morgan’s Laws
We can build any circuit using just NAND or NOR gates!

## Slide 23: Majority Vote Circuit
Create a truth table with input variables (A, B, C) that represent the vote (yeah or nay) of three people
Design a circuit that emits 1 as output if and only if at least 2 out of the 3 input lines are also 1
  Start out by making a truth table for all 8 possible input permutations
  Then use AND gates to select only those input permutations that that represent valid (1/high/true) “majority” output
  Then use OR gates to gather the output of those AND gates into a single output line

## Slide 24: Majority Vote Circuit
1
0
1
0
0
1
0
1
1

## Slide 25: Binary Addition

## Slide 26: Full Adder Circuit using NAND gates

## Slide 27: Chaining Full Adders with Ripple Carry
1 0 1 = 5
1 1 0 = 6
0 1 1
1
= 11
2
10
2
10
2
10
1
0
0
1
1
1
1
1
0
0
0
1

## Slide 28: 1 Bit Memory : Set-Reset Latch
The key was to send the output back into the input!

## Slide 29: 1 Bit Memory: A clocked J-K Flip-flop
A J-K flip-flop can be set/reset/toggled only during the rising edge of the clock signal
When the clock is low a latch maintains its prior output value

## Slide 30: CD4027 Dual J-K Flip-Flop
CD4027BE
+5V
GND

## Slide 31: A 4-Bit Counter Using Clocked J-K Flip-Flops
+5V
+5V
+5V
+5V
LSB
MSB

## Slide 32: Reading 3 bits from a memory with 4 addresses
Address Lines
Data Lines
This 12-bit memory
is made from a 4 x 3 matrix of flip-flops
Consider that a typical 256 GB
smart phone has
bits of memory!

## Slide 33: A Computer = An Adder with Memory

## Slide 34: Apollo Guidance Computer

## Slide 35: Apollo Guidance Computer

## Slide 36: Digital Logical Simulator

## Slide 37: Install Oracle Java Standard Edition
https://www.oracle.com/java/technologies/downloads

## Slide 38: Oracle Java SE – Microsoft Windows
https://download.oracle.com/java/20/latest/jdk-20_windows-x64_bin.msi

## Slide 39: Oracle Java SE – Apple macOS
https://www.oracle.com/java/technologies/downloads/#jdk20-mac

## Slide 40: Oracle Java SE – Ubuntu Linux
https://www.oracle.com/java/technologies/downloads/#jdk20-linux

## Slide 41: Design App – Digital Circuit Simulator
https://github.com/hneemann/Digital
Create a new subfolder in your $HOME folder called Digital and extract the ZIP file contents into that new subfolder

## Slide 42: Launch Digital App




## Slide 43: Launch Digital App

## Slide 44: Simple Circuit

## Slide 45: Pick AND Gate

## Slide 46: Drag AND Gate

## Slide 47: Place AND Gate
Single LEFT click to place a component

## Slide 48: Pick NOT Gate

## Slide 49: Drag NOT Gate

## Slide 50: Place NOT Gate
Single LEFT click to place a component

## Slide 51: Pick OR Gate

## Slide 52: Place OR Gate

## Slide 53: Place 2nd AND Gate

## Slide 54: Place 2nd NOT Gate

## Slide 55: Pick Input Signal

## Slide 56: Drag Input Signal

## Slide 57: Place Input Signal

## Slide 58: Place 2nd Input Signal

## Slide 59: Place 3rd Input Signal

## Slide 60: Place 4th Input Signal

## Slide 61: Pick Output Signal

## Slide 62: Place Output Signal

## Slide 63: Wire Up 1st Input to 1st AND Gate
Single LEFT click
on the output pin of the 1st INPUT

## Slide 64: Wire Up 1st Input to 1st AND Gate
Move mouse leftward
(while NOT holding LEFT button)
to the top input pin of the
1st AND Gate

## Slide 65: Wire Up 1st Input to 1st AND Gate
Single LEFT click (to end wire drawing mode) and the wire should turn dark blue

## Slide 66: Wire Up 1st Input to 1st AND Gate

## Slide 67: Wire Up Output of 1st AND to 1st OR Gate

## Slide 68: Wire Up Output of 1st AND to 1st OR Gate
Moving mouse DOWN
makes the wire
"turn" the corner

## Slide 69: Wire Up Output of 1st AND to 1st OR Gate
Single LEFT click starts a new wire direction

## Slide 70: Wire Up Output of 1st AND to 1st OR Gate
Single LEFT click (to end wire drawing mode) and the wire should turn dark blue

## Slide 71: Wire Up 3rd Input to 1st NOT to 1st OR Gate

## Slide 72: Draw Bounding Rectangle to Select Wire(s)
After selecting the wire press DEL key

## Slide 73: Draw Bounding Rectangle to Select Wire(s)
After selecting the wire(s) press DEL key

## Slide 74: Wire Up OR Gate to 2nd AND Gate

## Slide 75: Wire Up 4th Input to 2nd AND Gate

## Slide 76: Wire Up 2nd AND to 2nd NOT Gate

## Slide 77: Wire Up 2nd NOT to OUTPUT Signal

## Slide 78: Label 1st Input Signal
Right click on Input Symbol

## Slide 79: Label 2nd Input Signal
Right click on Input Symbol

## Slide 80: Label 3rd and 4th Input Signals

## Slide 81: Label Output Signal
Right click on Output Symbol

## Slide 82: Label Output Signal

## Slide 83: Select Analysis Menu Option

## Slide 84: Generate Truth Table for Circuit

## Slide 85: Save Circuit File

## Slide 86: Save Circuit File

## Slide 87: Open Majority Vote Circuit

## Slide 88: Open Majority Vote Circuit

## Slide 89: Generate Truth Table for Majority Vote Circuit

## Slide 90: Generate Truth Table for Majority Vote Circuit

## Slide 91: Boolean Logic Gates As Matrices
We can represent the classical bits 0 and 1 as (2 x 1) vectors
We can also represent classical logic gates as matrices

## Slide 92: Boolean Logic Gates As Matrices
We can apply a NOT gate to bit via matrix multiplication
But the classical AND and OR gates require two inputs
  Represented as matrices, the AND gate and OR gate each have a shape 2 x 4 and therefore must act on a vector of shape 4 x 1
  The matrix multiplication will produce a 2 x 1, which is a classic bit vector, matching the fact those two gates each have one output line
NOT
0
1
NOT
1
0
2 x 2
2 x 1
2 x 1

## Slide 93: Tensor Products

## Slide 94: Tensor Products
A vector than can be written as the tensor of two vectors is called separable
A vector than cannot be written as the tensor of two vectors is called entangled
There are no values for that will produce the required vector

## Slide 95: Tensor Products
2 x 2
3 x 3

## Slide 96: Tensor Products
2 x 2
3 x 3
6 x 6

## Slide 97: Tensor Products
0
0
A = 0, B = 0
0
1
A = 0, B = 1
1
0
A = 1, B = 0
1
1
A = 1, B = 1
We can encode the state of two classical bits into one vector using the tensor product

## Slide 98: Boolean Logic Gates As Matrices
We can now apply the AND gate using two encoded input bits and calculate a single output bit
1
0
T
F
A = 1, B = 0
AND
(T, F)

## Slide 99: Boolean Logic Gates As Matrices
We can now apply the AND gate using two encoded input bits and calculate a single output bit
AND
(T, T)
1
1
T
T
A = 1, B = 1

## Slide 100: Boolean Logic Gates As Matrices
We can now apply the OR gate using two encoded input bits and calculate a single output bit
0
0
F
F
A = 0, B = 0
OR
(F, F)

## Slide 101: Boolean Logic Gates As Matrices
We can now apply the OR gate using two encoded input bits and calculate a single output bit
OR
(T, F)
1
0
T
F
A = 1, B = 0

## Slide 102: Boolean Logic Gates As Matrices
We can also combine gates via matrix multiplication, and produce a universal gate like NAND
2 x 2
2 x 4
2 x 4

## Slide 103: Run Cell 1 – gate_matrices.ipynb
0
1
0
1






## Slide 104: Run Cell 2 – gate_matrices.ipynb







## Slide 105: Run Cell 3 – gate_matrices.ipynb



We can encode the state of two classical bits into one vector using the tensor product
Leopold Kronecker
(1823-1891)
a b
0 0
0 1
1 0
1 1
a b
0 0
0 1
1 0
1 1
a b
0 0
0 1
1 0
1 1
a b
0 0
0 1
1 0
1 1

## Slide 106: Run Cell 4 – gate_matrices.ipynb



Represented as a matrix, the AND gate has a shape 2 x 4 and therefore must act on a vector of shape 4 x 1
The matrix multiplication will produce a 2 x 1, which is a classic bit vector, matching the fact the AND gate has one output line

## Slide 107: Run Cell 5 – gate_matrices.ipynb



Represented as a matrix, the OR gate has a shape 2 x 4 and therefore must act on a vector of shape 4 x 1
The matrix multiplication will produce a 2 x 1, which is a classic bit vector, matching the fact the OR gate has one output line

## Slide 108: Run Cell 6 – gate_matrices.ipynb



Note: We multiply the gate matrices in reverse order than they appear in the circuit diagram

## Slide 109: Simulating a Simple Circuit Using Matrices
We can now simulate more complex circuits using tensor products to "link" multiple input lines and matrix multiplication to represent the action of Boolean gates on those input states

## Slide 110: Run Cell 1 – simple_circuit.ipynb









## Slide 111: View Cell 2 – simple_circuit.ipynb
g1
g2
g3
g4
g5








## Slide 112: View Cell 2 – simple_circuit.ipynb








## Slide 113: Run Cell 2 – simple_circuit.ipynb

## Slide 114: Session 21 – Know You Know…
Digital Logic Circuits
  All computers are made from chains of simple logic gates
  NAND and NOR gates are universal → they can make all other classical Boolean logic gates!
How a computer performs arithmetic = full adders
  Subtraction is just addition with inverted logic
  Multiplication is just repeated addition
  Division is just repeated subtraction
How a computer stores numbers in memory = flip-flops
  Four gates make a bit, eight bits make up a byte
  Imagine how many gates are in your 128GB smartphone!

## Slide 115: Session 21 – Know You Know…
The tensor (Kronecker) products combine individual classical bits into a separable state vector
  A two-bit system can be represented by a 4 x 1 state vector
A two-bit zero state is not [0,0,0,0] but rather [1,0,0,0]
  You must think in terms of index numbers, not element values
  Zero is a thing, zero counts = the first element is at index zero
  Therefore, a zero is [1,0,0,0] because it has a 1 in the first element
We can represent Boolean logic gates as 2 x 4 matrices
  We apply logic operators to state vectors using matrix multiplication – we "dot" the gate matrix into the input state vector
  We can compose gates by dotting each gate’s action operator

## Slide 116: Task 21-01
Create a Jupyter Lab Notebook called octal_converter.ipynb
In cell 1, convert the octal number 2323 to base 10 (decimal) by looping, and display both numbers
In cell 2, convert the decimal number you calculated in cell 1 back to octal by looping, and display both numbers
In cell 3, convert the octal number 2323 to base 10 (decimal) without looping, and display both numbers
In cell 4, convert the decimal number you calculated in cell 3 back to octal without looping, and display both numbers
Upload your solution to the BNL QIS101 SharePoint site

## Slide 117: Task 21-02
Using the Digital App, create a circuit file called full_adder.dig
  Using only 1 OR, 2 AND, 2 XOR gates, plus five I/O pins, design a FULL ADDER circuit
  The circuit has 3 input lines, and 2 output lines to indicate the sum and if there needs to be a carry to the next column
  Verify your circuit by having Digital create a truth table
Upload to the BNL QIS101 SharePoint site your circuit (.dig) file

## Slide 118: Task 21-03
Create a Jupyter Lab Notebook called majority_vote.ipynb to simulate the circuit and generate the truth table of the majority vote circuit shown on slide #24
In Cell 1, declare all the necessary arrays for the Boolean states and logic gates required to simulate all permutations of input and output states
In Cell 2, implement the complete classical digital logic circuit using Numpy matrix algebra functions
In Cell 3, generate and display the full truth table for the circuit
Upload your solution to the BNL QIS101 SharePoint site